/* Program Example 12.1: Bluetooth serial test data program

*/

#include "mbed.h"

Serial rn41(p9,p10);

BusOut led(LED4,LED3,LED2,LED1);

int main() {

rn41.baud(115200);     // set baud for RN41

while (1) {

for (char x=0x30;x<=0x39;x++){  // ASCII numerical characters 0-9

rn41.putc(x);                 // send test char data on serial

led = x & 0x0F;               // set LEDs to count in binary

wait(0.5);

}

}

}

Program Example 12.1: Bluetooth serial spammer

/* Program Example 12.2: Bluetooth serial sniffer program

*/

#include "mbed.h"

Serial rn41(p9,p10);

BusOut led(LED4,LED3,LED2,LED1);

int main() {

rn41.baud(115200);           // setup baud rate

rn41.printf("Serial sniffer: outputs received data to LEDs\n\r");

while (1) {

if (rn41.readable()) {     // if data available

char x=rn41.getc();      // get data

led=x;                   // output LSByte to LEDs

}

}

}

Program Example 12.2: Bluetooth serial sniffer program

/*Program Example 12.3: function to initialise paired Bluetooth connection with RN-41 modules

*/

void initialise_connection() {

rn41.putc('$');    // Enter command mode

rn41.putc('$');    //

rn41.putc('$');    //

wait(0.5);

rn41.putc('C');    //

rn41.putc(',');    // Send MAC address

rn41.putc('0');    //

rn41.putc('0');    //

rn41.putc('0');    //

rn41.putc('6');    //

rn41.putc('6');    //

rn41.putc('6');    //

rn41.putc('0');    //

rn41.putc('7');    //

rn41.putc('A');    //

rn41.putc('C');    //

rn41.putc('C');    //

rn41.putc('1');    //

wait(0.5);

rn41.putc('-');    // Exit command mode

rn41.putc('-');    //

rn41.putc('-');    //

rn41.putc(0x0D);   //

wait(0.5);

}

Program Example 12.3: Function to initialise paired Bluetooth connection with RN-41 modules

/* Program Example 12.4: Paired Bluetooth master program

*/

#include "mbed.h"

Serial rn41(p9,p10);

BusOut led(LED4,LED3,LED2,LED1);

DigitalIn Din(p26);                // digital switch input on pin 14

char x;

void initialise_connection(void);

int main() {

rn41.baud(115200);

initialise_connection();

while (1) {

if (Din==1) {            // if digital input switched high

x=0x0F;              // override with 0x0F

} else {

x++;                 // else increment and

if (x>0x0F) {        // output count value

x=0;

}

}

rn41.putc(x);            // send char data on serial

led = x;                 // set LEDs to count in binary

wait(0.5);

}

}

// add function initialise_connection code here...

Program Example 12.4: Paired Bluetooth master program

/* Program Example 12.5: Emulating a USB mouse

*/

#include "mbed.h"                      // include mbed library

#include "USBMouse.h"                  // include USB Mouse library

USBMouse mouse;                        // define USBMouse interface

int dx[]={40,0,-40,0};                 // relative x position co-ordinates

int dy[]={0,40,0,-40};                 // relative y position co-ordinates

int main() {

while (1) {

for (int i=0; i<4; i++) {      // scroll through position co-ordinates

mouse.move(dx[i],dy[i]);   // move mouse to co-ordinate

wait(0.2);

}

}

}

Program Example 12.5: Emulating a USB mouse

/* Program Example 12.6: MIDI messaging with variable scroll speed

*/

#include "mbed.h"

#include "USBMIDI.h”

USBMIDI midi;                        // initialise MIDI interface

AnalogIn Ain(p19);                   // create analog input

int main() {

while (1) {

for(int i=48; i<72; i++) {                 // step through notes

midi.write(MIDIMessage::NoteOn(i));    // note on

wait(Ain);                             // pause

midi.write(MIDIMessage::NoteOff(i));   // note off

wait(2*Ain);                           // pause

}

}

}

Program Example 12.6: MIDI messaging with variable scroll speed

/* Program Example 12.7: Ethernet write

*/

#include "mbed.h"

#include "Ethernet.h"

Ethernet eth;                   // The Ethernet object

char data[]={0xB9,0x46};        // Define the data values

int main() {

while (1) {

eth.write(data,0x02);   // Write the package

eth.send();             // Send the package

wait(0.2);              // wait 200 ms

}

}

Program Example 12.7: Ethernet write

/* Program Example 12.8: Ethernet read

*/

#include "mbed.h"

Ethernet eth;                          // Ethernet object

Serial pc(USBTX, USBRX);               // tx, rx for host terminal coms

char buf[0xFF];                        // create a large buffer to store data

int main() {

pc.printf("Ethernet data read and display\n\r");

while (1) {

int size = eth.receive();              // get size of incoming data packet

if (size > 0) {                        // if packet received

eth.read(buf, size);                 // read packet to data buffer

pc.printf("size = %d data = ",size); // print to screen

for (int i=0;i<size;i++) {           // loop for each data byte

pc.printf("%02X ",buf[i]);         // print data to screen

}

pc.printf("\n\r");

}

}

}

Program Example 12.8: Ethernet read

/* Program Example 12.9: mbed HTTP client test

*/

#include "mbed.h"

#include "EthernetNetIf.h"

#include "HTTPClient.h"

EthernetNetIf eth(

IpAddr(192,168,0,101),    //IP Address

IpAddr(255,255,255,0),    //Network Mask

IpAddr(192,168,0,1),      //Gateway

IpAddr(192,168,0,1)       //DNS

);

HTTPClient http;

HTTPText txt;

Serial pc (USBTX,USBRX) ;

int main() {

pc.printf("\r\nSetting up network connection...\n\r");

eth.setup();

pc.printf("\r\nSetup OK. Queerying data...\r\n");

// attempt to access file ‘mbedclienttest.txt’ through the internet...

HTTPResult r=http.get("http://www.rt60.co.uk/mbed/mbedclienttest.txt", &txt);

pc.printf("Result :\n\r\"%s\"\n\r", txt.gets());

}

Program Example 12.9: mbed HTTP client test

/* Program Example: 12.10 mbed file server setup

*/

#include "mbed.h"

#include "EthernetNetIf.h"

#include "HTTPServer.h"

LocalFileSystem fs("webfs");

EthernetNetIf eth(

IpAddr(192,168,0,101),      //IP Address

IpAddr(255,255,255,0),      //Network Mask

IpAddr(192,168,0,1),        //Gateway

IpAddr(192,168,0,1)         //DNS

);

HTTPServer svr;

int main() {

eth.setup();

FSHandler::mount("/webfs", "/");    //Mount webfs path on root path

svr.addHandler<FSHandler>("/");     //Default handler

svr.bind(80);

while(1)

{

Net::poll();                  // poll for internet data exchange requests

}

}

Program Example 12.10 mbed file server setup

/* Program Example 12.11 Remote Procedure Calls example

*/

#include "mbed.h"

#include "EthernetNetIf.h"

#include "HTTPServer.h"

LocalFileSystem fs("webfs");

EthernetNetIf eth(

IpAddr(192,168,0,101),                  //IP Address

IpAddr(255,255,255,0),                  //Network Mask

IpAddr(192,168,0,1),                    //Gateway

IpAddr(192,168,0,1)                     //DNS

);

HTTPServer svr;

DigitalOut led1(LED1, "led1");            // define mbed object

int main() {

Base::add_rpc_class<DigitalOut>();      // RPC base command

eth.setup();                            // Ethernet setup

FSHandler::mount("/webfs", "/");        // Mount /webfs path on root

svr.addHandler<FSHandler>("/");         //Default handler

svr.addHandler<RPCHandler>("/rpc");     // Define RPC handler

svr.bind(80);

while(1)

{

Net::poll();

}

}

Program Example 12.11 Remote procedure calls example

/* Program Example 12.12 Using RPC variables for remote mbed control

*/

#include "mbed.h"

#include "EthernetNetIf.h"

#include "HTTPServer.h"

#include "RPCVariable.h"

#include "SerialRPCInterface.h"

LocalFileSystem fs("webfs");

EthernetNetIf eth(

IpAddr(192,168,0,101),//IP Address

IpAddr(255,255,255,0),//Network Mask

IpAddr(192,168,0,1),  //Gateway

IpAddr(192,168,0,1)   //DNS

);

HTTPServer svr;

DigitalOut Led1(LED1);              // define mbed object

DigitalIn Button1(p21);             // button

int RemoteLEDStatus=0;

RPCVariable<int> RPC_RemoteLEDStatus(&RemoteLEDStatus,"RemoteLEDStatus");

int RemoteLED1Button=0;

RPCVariable<int> RPC_RemoteLED1Button(&RemoteLED1Button,"RemoteLED1Button");

int main() {

Base::add_rpc_class<DigitalOut>();        // RPC base command

eth.setup();                              // Ethernet setup

FSHandler::mount("/webfs", "/");   // Mount /webfs path root path

svr.addHandler<FSHandler>("/"); //Default handler

svr.addHandler<RPCHandler>("/rpc");       // Define RPC handler

svr.bind(80);

printf("Listening...\n");

while (true) {

Net::poll();

if ((Button1==1)|(RemoteLED1Button==1)) {

Led1=1;

RemoteLEDStatus=1;

} else {

Led1=0;

RemoteLEDStatus=0;

}

}

}

Program Example 12.12 Using RPC variables for remote mbed control